## Slide 1: Unit 1 Data Types and Combinational Logic
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Represent signals in SystemVerilog of various types:
  Logical vectors and signed and unsigned integers
Implement arithmetic operations (additions, multiplications, bit operations)
Identify cases for overflow and truncation
Create simple combinational logic modules to implement functions
Draw a block diagram representation of the module

## Slide 3: Outline
Basic Data Types: Logic and Integers
Truncation and Overflows
Bit Shifts
Simple Combinational Logic

## Slide 4: Hardware Description Language
Hardware Description Language (HDL)
  Example: Verilog, SystemVerilog
  Describes hardware structure and behavior
  Items natively run in parallel
  Code is synthesized
  Code becomes to logic elements, registers, …
  Also become testbenches
Software
  Example: C, python
  Describes sequential behavior
  One instruction after another
  Code is compiled
  Becomes machine code for a processor

## Slide 5: System Verilog vs Verilog
Verilog
  Created in 1983-84
  Standardized in 1995. Became mainstream RTL
  Largely used for legacy designs
System Verilog (this unit)
  Developed in 2002
  Extends Verilog
  Better abstraction, parameterization
  Significantly improved testbench
  Overwhelming design choice today

## Slide 6: Logic and Logic Vectors
Logic: Basic data type in System Verilog
  Value 0, 1, X or Z
  X = unknown or unspecified
  Z = not connected
  We will discuss X and Z later
Logic vector
  A group of log bits
  Each vector has a bit width.

## Slide 7: Bitwise Operations
System Verilog has natural ways to pack and unpack bits
Note bits are always counted from 0

## Slide 8: Example Problem

## Slide 9: Solution

## Slide 10: Integers
Integers can be regarded naturally as logic vectors
Vector bit width will determine the range of the integer
Must indicate if the value is signed or unsigned:
  Unsigned bits. Represents a value in
  Signed bits: Represents a value in
Example with bits
  Unsigned range is 0, …, 255.
  Signed range is -128, …, 127

## Slide 11: Two Complement
Signed values are represented with two complement
Suppose is represented by a -bit signed integer
  Range
  : the “sign” bit
  : the “lower” bits
For
  Sign bit
  Lower bits:
For
  Sign bit
  Lower bits:
Sign bit
Lower bits

## Slide 12: Example Problem

## Slide 13: Two’s Complement = Modulo Arithmetic
Two’s complement is equivalent to modulo arithmetic
Modulo equality: Integers and are equal module :
Example:
  mod 16
Given any , its -bit two’s complement representation is the unique with:
Example: Find the following bits two’s complement representations:
  (since is already in range )

## Slide 14: System Verilog Literals and Constants
Literal: A value written directly in code (not stored in a storage element)
  Constant. Does not change
SV has a specific syntax: <size>'<base><digits>
  <size> = number of bits. If omitted, takes a default value, typically 32-bits
  <base> = b, o, d, h : binary, octal, decimal, hex
  <digits> = value
Examples:
  8'd13 → 8‑bit decimal 13
  8'b0101_1010 → 8‑bit binary
  4'hF → 4‑bit hex (1111)
  16'd8 → 16‑bit decimal 8
  8'b0101 → 8‑bit binary 0101
  -8'd5 → 5-bit two-complement decimal -5 (11111011)

## Slide 15: Example Problem

## Slide 16: Outline
Basic Data Types: Logic and Integers
Truncation and Overflows
Bit Shifts
Simple Combinational Logic

## Slide 17: Truncation
Occurs when a variable is assigned a value out of range
In above code we need
When is outside this range, SystemVerilog will truncate:
  Take the LSBs of
  Sign extend if necessary
Equivalent to

## Slide 18: Sample Problem

## Slide 19: Solution using Binary Representations

## Slide 20: Solution using Modulo Arithmetic

## Slide 21: Simulating Truncation in Python
This code works for numpy arrays
Mask the LSB
Then sign extend if necessary

## Slide 22: Saturation
Truncation results in values far different from original
  Ex: Truncate to 4 signed bits
Alternatively, can saturate
  Clip to max or min values before assignment
  Ex: Truncate 9 to 7
  Provides less approximation error
  But adds a bit of extra logic
Example to right:
  Want to assign

## Slide 23: Addition Overflow Rules
Consider adding
If and are both signed or both unsigned:
  No overflow requires
  bit width of
If is signed and is unsigned,
  No overflow requires
  Example if (4 bits signed), (4 bits unsigned)
  Sum is which needs 6 bits signed.

## Slide 24: Addition in System Verilog
SV does not auto-promote with addition
Adding in SV:
  Sum is stored in temporary
  No additional bit
  May overflow before assignment
To avoid overflow:
  Method 1: Add one term at a time
  Method 2: Extend then add

## Slide 25: Sample Problem

## Slide 26: Multiplication Overflow
Consider multiplying
  and may be signed or unsigned
To prevent overflow, we need:
SV implementation
  Unlike addition, SV auto-promotes
  Stores product in sufficiently large bit width
  Will then truncate if needed on assignment

## Slide 27: Sample Problem

## Slide 28: Summary
Two integer types: = signed integers = unsigned
Each has finite range
Assignments outside that range result in overflow
In case of overflow, system Verilog performs truncation
Optionally, you can add code to explicitly saturate
  Offers better performance but adds additional logic
Arithmetic operations result in bitwidth growth
  Addition of 2 numbers requires 1 extra bit
  Multiplication of 2 numbers requires width = product of the two numbers

## Slide 29: Outline
Basic Data Types: Logic and Integers
Truncation and Overflows
Bit Shifts
Simple Combinational Logic

## Slide 30: Logical Bit Shift
Bit shift operators:
  and Right and left shift by bits
  Fills in with zeros
Bit widths always stay the same.
  Hence, bits may be lost
Examples:
  (
  (

## Slide 31: Logical Shift and Bit Widths
Caution:
  Logical bit shifts do not change width
  Some bits may be discarded
To avoid discarding:
  Widen first, then shift

## Slide 32: Arithmetic Shift
Logical Shift Changes Negative Values to Positive
  Since leading MSBs are filled with zeros
  Example: Suppose as an 8-bit signed number
  Then
Arithmetic shift
  Fills in leading MSBs with sign bit
  Written in SV with >>>
  Ex: >>>

## Slide 33: Python vs. SV
Operation | System Verilog syntax | Python syntax
Left shift (Logical or arithmetic) | or | 
Arithmetic right shift |  | 
Logical right shift = number of bits in destination |  | 
Operation | System Verilog syntax | Python syntax
Left shift (Logical or arithmetic) | or | 
Arithmetic right shift |  | 
Note: All shifts in python are arithmetic
To emulate logical right shift need a mask

## Slide 34: Arithmetic Shift and Powers of Two
Arithmetic shifts approximate multiplication by powers of two
Left shift:
  Assuming the MSBs are not discarded
  Or the value is extended by bits prior to left shift
Right shift: >>>
  Only approximate since the LSBs will be discarded
  So, there is a loss in precision

## Slide 35: Example Problem

## Slide 36: Solution

## Slide 37: Outline
Basic Data Types: Logic and Integers
Truncation and Overflows
Bit Shifts
Simple Combinational Logic

## Slide 38: Module and Combinational Logic
Module: A named circuit block with some inputs and outputs
  Fully self-contained
  Takes some input signals and produces some outputs
  May have sub-modules
Combinational logic: Outputs depend only on current inputs
  No memory
  No storage
  We will contrast this type of module with sequential logic in the next unit

## Slide 39: Simple Example: ReLU + Linear
Goal: Implement a combinational logic module for the function
  Linear function + ReLU
  Used widely in machine learning
Output port
Input ports

## Slide 40: SystemVerilog Description
Each block is a module
  Has inputs and outputs
  Logical mapping from inputs to outputs
Description is behavioral only
  Does not say how it will be implemented
  We discuss that later

## Slide 41: Module Components in SV
Module name
Ports:
  Defines inputs and outputs
  Each has a type (more detail later)
Behavioral description
  In this case, a combinational block
  Sequence of operations
  From input to output

## Slide 42: Block Diagram
Function of a module typically represented by a block diagram
Graphical representation of a potential implementation
Typically, diagram is at high-level
  Adders, multipliers not low-level details components like gates

## Slide 43: Problem
Assigned as homework
Note there is a conservative and more precise bit width analysis
  Both will receive full credit