## Slide 1: Unit 2 Sequential Logic and FSMs
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Define finite state machines and identify inputs, outputs, and states
Implement FSMs with sequential logic in SystemVerilog
Break and implement functions over multiple clock cycles
Write a testbench for the hardware modules
Simulate, and synthesize the SystemVerilog using Vivado tools

## Slide 3: Outline
Registers, Clocks and Sequential Logic and Finite State Machines
Splitting Long Computations
Simulating and Synthesizing Simple Modules in Vivado

## Slide 4: Limitations of Combinational Logic
No memory — cannot store past values
Output changes immediately with input changes (no control over timing)
Long combinational paths lead to large propagation delays
Hard to build large systems without controlled timing boundaries
Glitches and hazards can propagate freely
No notion of “steps” or “cycles” — everything is continuous

## Slide 5: Synchronous (Sequential) Logic
Introduces state via flip‑flops or registers
Breaks long logic into clocked stages, improving performance
Provides predictable timing — changes only occur on clock edges
Makes large systems modular and easier to reason about
Eliminates most hazards/glitches from propagating across stages
Enables pipelining, finite‑state machines, and sequential algorithms
Allows clean interfaces between modules (valid/ready, handshakes, etc.)
Synchronous logic is the dominant paradigm for design

## Slide 6: Clock Signal
Clock: An alternating binary signal
  Visualized as a square wave
Each period is called a clock cycle
  Typically, between two rising edges
Parameters:
  Clock period
  Frequency
Typical parameters:
  FPGA logic: 100 to 500 MHz
  ASIC: 500 MHz to 1 GHz

## Slide 7: Synchronous Logic Example: Counter
Synchronous logic:
  Updates occur on each clock cycle
Simple example: A down-counter
Potential specification: On clock cycle :
  If and
  Else
 | s |  | 
0 | 0 | X | 0
1 | 1 | 3 | 0
2 | 0 | 0 | 3
3 | 1 | 6 | 2
4 | 0 | 0 | 1
5 | 0 | 0 | 0
6 | 1 | 5 | 0
7 | 1 | 5 | 5
8 | 0 | 0 | 4
9 | 0 | 0 | 3
0 | 0 | X | 0
1 | 1 | 3 | 0
2 | 0 | 0 | 3
3 | 1 | 6 | 2
4 | 0 | 0 | 1
5 | 0 | 0 | 0
6 | 1 | 5 | 0
7 | 1 | 5 | 5
8 | 0 | 0 | 4
9 | 0 | 0 | 3

## Slide 8: Key Components of a Module
Counter example from previous slide:
  If and
  Else
Inputs: and
  What the module takes as input
Output:
  What the module produces
State:
  What needs to be stored to compute the subsequent outputs given the inputs

## Slide 9: What is a State?
Definition: A state is a set of variables such that:
  Given and inputs
  Outputs are fully determined
In our case:
  is the state
  Given and future inputs and
  We can fully determine future outputs

## Slide 10: Synchronous Logic as an FSM
General finite state machine
Update function:
  Describes how the state evolves
Output function:
State
Update and output functions
O
Input
Statestate_next[k]

## Slide 11: Building an FSM in Hardware
States are stored in registers
  Basic storage element
Update and output functions
  Implemented in combinational logic
  No storage
  Takes input and current state
  Produces next state and output
  Must finish within one clock cycle
State
Update and output functions
O
Input
Statestate_next[k]
Registers (clocked)
Combinational logic (no clock)
Clock

## Slide 12: Register Physical Model
Basic storage element in synchronous logic
On each rising edge of clk:
  Assigns xreg to x
Value of xreg is maintained even if x changes
Example below: Input is “sampled” at rising edges

## Slide 13: Register: Discrete-Time Model
Suppose input has value in clock cycle
Then register output is:
  A simple delay element
Example:
  If in clock cycles 0 to 4
  Suppose is initialized in clock cycle 0
  Then = 0, 4, 8, 9, 1, 2 in clock cycles 0 to 5

## Slide 14: Writing the Counter in System Verilog
The counter is a module
The module definition describes:
  Inputs and outputs
  Must have a clock input
  Typically, also a reset
Does not need the internal state
  Unless it happens to be an output

## Slide 15: Counter Main Body
Combinational block (always_comb)
  Takes current state and input
  Describes next state and output
always_ff
  Registers values for next state

## Slide 16: Putting it Together
We now have the FSM description
Three parts
Module declaration
  Inputs, outputs
Always_comb block
  Describes next state
Always_ff block
  Updates state from next_state

## Slide 17: Blocking vs. Non-Blocking
Blocking assignment
  Use = in SV
  Performed sequentially
  Assigns temporary (i.e., non-state variables)
  Used in always_comb or always_ff block
Non-blocking assignment
  Use <= in SV
  Assigns registers / states
  Only in always_ff block
  Always update in parallel

## Slide 18: Example Problem

## Slide 19: Try Answer on LLM Auto-Grader
Use AI to get instant feedback
Enter your answer
Hit Grade

## Slide 20: Solution: FSM Model
Write the FSM model
Remember: Updates in always_ff are in parallel
  Test is based on current cycle value, not next cycle
Equivalent FSM model
if
else if (
0 | 15 | 10
1 | 25 | 10
2 | 35 | 10
3 | 45 | -10
4 | 35 | -10
5 | 25 | -10
0 | 15 | 10
1 | 25 | 10
2 | 35 | 10
3 | 45 | -10
4 | 35 | -10
5 | 25 | -10

## Slide 21: In-Class Exercise
Try answering on the auto-grader

## Slide 22: Outline
Registers, Clocks and Sequential Logic and Finite State Machines
Splitting Long Computations
Simulating and Synthesizing Simple Modules in Vivado

## Slide 23: Synchronous Version of ReLU + Linear
Recall early combinational example
A potential synchronous version could work as follows
On each clock cycle:
  Register input to a state
Output combinationally from
Why?
  Output computation has a full clock cycle
  Output is in a known state by the end of each clock cycle

## Slide 24: Synchronous Module Declaration
Making module synchronous is easy
First add two inputs to ports
  Clock signal
  Reset
Clock
Reset

## Slide 25: System Verilog Main Body
Synchronous logic has two parts
always_ff:
  Assigns register outputs
  All operations are in parallel (non-blocking)
  Our example: Saves inputs to registers
always_comb:
  Assigns signals via combinational logic
  Operations are sequential (blocking)
  Our example: Computes output from registered inputs

## Slide 26: Synchronous Block Diagram
Inputs are registered
Output is combinational from input

## Slide 27: FSM Description
States:
Combinational statements:
State updates:
Putting it together:
  Desired output with one cycle delay

## Slide 28: A More Complex Example
Consider a quadratic function:
For simplicity, assume are fixed parameters
Single cycle implementation to the right

## Slide 29: Problems with Single Cycle Implementation
Problem: Each clock cycle has a “lot” to do
Longest path from has:
  Compute : One multiply
  Compute : One multiply
  Add : One addition
  We will discuss finding longest paths in detail later
In general, two multiplications in one clock cycle is hard
Typically, we limit to one multiplication
  More on this later

## Slide 30: A Two Cycle Design
We can reduce the computation per cycle by breaking operation in two cycles
Register two intermediate terms:
  xsq = xreg * xreg
  lin_term = w1*xreg + w0

## Slide 31: Analysis
Registers:
Updates:
Substituting in values:
So, output matches desired equation
  But at a two cycle delay

## Slide 32: In Class Problem
Hint:
  Write the computation graph for
  Add registers at input and intermediate variables

## Slide 33: Outline
Registers, Clocks and Sequential Logic and Finite State Machines
Splitting Long Computations
Simulating and Synthesizing Simple Modules in Vivado

## Slide 34: Building the Hardware Roadmap
Design
Functional simulation
Synthesis
Next steps
Design:
  Write a behavioral description (e.g., in SV)
  What should the module should do exactly?
Functional simulation
  Validate module does what it is supposed to do?
  Logical mapping from inputs to outputs
Synthesis
  Map the description into real hardware
  Gates, FPGA components, …
Next steps
  Place route, timing analysis, bitstreams, …
This unit
Later units…

## Slide 35: Linear+ReLU Example
All files in github repo: hwdesign/demos/fsm
Define counter in file counter.sv

## Slide 36: Next Step: Build a Testbench
Testbench
  A second SV module
  Connects to device under test (i.e, module we want to test)
  TB provides DUT inputs
  TB verifies DUT outputs are correct
Inputs
Outputs
Testbench tb_lin_rely.sv
DUT lin_relu.sv

## Slide 37: Testbenches are not Synthesized
Testbenches are for simulation only
They will not be synthesized
Can include un-synthesizable constructs
  Print statements
  File read and write
  Complex data structures
Modern trend:
  Write TB in higher level language
  E.g., python
Inputs
Outputs
Testbench tb_lin_rely.sv
DUT lin_relu.sv

## Slide 38: Testbench Declaration
Testbench: a module to test the module
  Will not be synthesized
  Can have un-synthesizable constructs
  Ex: Read / write from file
Create a clock
Instantiate an instance of module to test
  Called the DUT = device under test
  Connect DUT to testbench signals

## Slide 39: Test Vectors
Create a set of test inputs
Loop through inputs
Put one new input each clock cycle
Testbench uses an initial construct
  Enables sequential set of events

## Slide 40: Initial Block
Runs once at time 0 of the simulation
  (or at its scheduled start time if delayed).
Statements inside run sequentially
  like a small program.
Not synthesizable for hardware
  Simulation‑only construct.
  Used for test benches
Concurrency:
  initial blocks and always blocks.

## Slide 41: Test Results
Test results outputs
Match expected values